Blue OS Developer

Daniel Wirick

4-7-19

# Document:
- Shall = Requirement
- Should = Desire
- KISP = Keep It Simple Please

# Project Goals:
- Easy to use (simple UI)
- Written in C (GUI in HTML5?, TCK, GTK, QT?)
- Minimal dependencies (maximize buildability)
- Build with GCC
- Makefile based (KISP)
- Version controlled with Git

Code Milestones:
Scheduler
Visual Task Allocator
Text Editor
Support File Generator
Board/Processor selector
Visual Resource Allocator
Shared Resource Configurator
Comment PDF tracking (register highlighting?)
Gcc Integration
Syntax highlighting
Keyword lookup
Debugger
Real Time OS Stats
Simulation

# Code Milestones
## Scheduler
    1. Scheduler General Requirements
      - Shall have a limit of 255 individual tasks
      - Shall generate a static schedule
      - Shall generate the schedule pre-task-runtime
      - Should provide easily understood errors if schedule fails
      - Should provide easily understood errors if input is invalid
      - Should provide easily understood errors if output can’t be generated
      - Shall allow input file name to be specified on the command line (-f <file name>)
      - Should optionally allow an output file path to be specified (-o <path>)
    1. Input File Requirements
      - Shall be in human readable format (preferably .txt)
      - Shall have a standard format
      - Shall specify the processor code space
      - Shall specify the processor ram
      - Shall specify the period of each task in tick units
      - Shall specify the run time for each task in tick units
      - Shall specify the start address of each task in code space
      - Shall specify the length of each task’s code space
      - Shall specify the start address of each task’s ram space
      - Shall specify the length of each task’s ram space
      - Shall specify the name of each task
      - Shall specify a sequential ID number for each task beginning with 0
      - Shall specify the length (in real time) for each tick
      - Should provide an ASCII task table header to assist users
      - Shall include the OS as the first task ID (0)
      - Should include the processor name
      1. Notes
        - See included Input_File_Example.txt
    1. Scheduling Requirements
      - Shall be exact rate
      - Shall be exact period
      - Should provide statistics for the schedule
      - Shall have a configurable length limit
      - Shall generate a schedule with task ID
      - Shall schedule the OS in any unfilled processor time
      - Shall provide statistics for the OS task
      - Shall provide a schedule of the shortest length (least common multiple)
      1. Notes:
        - The scheduler can schedule tasks beginning with the most frequent (smallest period) and finding places for each task in descending order of frequency. Other scheduling methods are acceptable if they meet the requirements.
    1. Output files requirements
      1. OS Linker File Requirements
        - Shall provide a linker file for Gcc’s LD that allocates OS’s code space
        - Shall allocate the first memory block to OS configuration
        - Shall include the vector table at the beginning of the OS section
        - Shall include the Task Table directly after the vector table
        - Shall allocate the rest of the OS memory for the OS code
        - Shall allocate sections on configurable memory boundaries
        - Shall allocate OS stack section in RAM matching
        1. Notes:
          - See included OS_Linker_Example.ld file
      1. Task Linker Files Requirements
        - Shall generate a linker file for each listed task, except OS
        - Shall allocate code and ram space matching the OS linker file
        - Shall allocate object files to sections
        - Shall assume object file names match task names
        - Shall use sections names that match task names
        1. Notes:
          - See included Task1_Linker_Example.ld and Task2_Linker_Example.ld
      1. Task Table and Schedule Requirements
        - Should provide an ASCII art of the schedule in comment form
        - Shall include the task list to associate task ID with code address
        - Shall include the task schedule
        - Shall follow a defined format
        1. Notes:
          - See included Schedule_Exmaple.txt